## Slide 1: Stream Monitoring 101
with the Clinton River Watershed Council

## Slide 2: MISSION
To protect, enhance, and celebrate the Clinton River, its watershed, and Lake St. Clair
Photos by: John Meyland
Clinton River Watershed Council
Non-profit organization
Supported by grants, individual membership, community membership, donations
Education
Stewardship
Watershed management

## Slide 3: The region draining into a river, river system, or other body of water.
What is a Watershed?

## Slide 4
Precipitation
Snowpack
Groundwater flow
Runoff – stormwater
Lakes
Tributaries
Forests
Farmland
Homes
Roads
Business
Factories
What’s IN a Watershed?

## Slide 5: Geography of the Watershed
Notes: This shows us a little bit of the geography of the Clinton River Watershed.

## Slide 6
No matter where you live, you live in a watershed!

## Slide 7
The Clinton!
What watershed do you live in?
Notes:   The Clinton!!!

## Slide 8
Urbanized
Rural / Residential
Rapidly Urbanizing

## Slide 9: About the Clinton River Watershed
760 square mile watershed
Portions of Lapeer, Macomb, Oakland & St. Clair counties
More than 60 communities
1.5 million people – most populous watershed in Michigan

## Slide 10
Stony
Creek
Upper
Clinton
ClintonMain
Red Run
North Branch
Clinton River East
Paint Creek
Major Subwatersheds
Rouge
River
Watershed
Notes: The Clinton River Watershed Council is divided into 7 Subwatersheds.

## Slide 11
Hold estimated 6 quadrillion gallons of water
Could cover the contiguous U.S. (48 States) with 9.5 ft. of water
Approximately one-fifth of world’s freshwater
90% of U.S. freshwater
3,288 miles of shoreline – more than Florida (1,197) and California (840)
94,000 square miles of water, drain twice as much land – Great Lakes Basin
WE ARE CONNECTED
About the Great Lakes Region
We are surrounded by precious fresh water

## Slide 12
Why do we care about the health of our rivers?

## Slide 13
Drinking Water
Recreation – 3rd largest marine industry
Economics – fishing, boating, tourism
Major local rivers – Huron, Rouge, Clinton
Steelhead Fishery
Scenic River Trails & Vistas
Local History
Place We Call Home
But threats exist…

## Slide 14
Industry?
Individuals ?
Who affects the health of the river?

## Slide 15
CWA - 1972
Point source pollution can be traced back to a specific location, such as a pipe or disposal site.

## Slide 16
Non-point source pollution is harder to trace.
Notes: Large amounts of pollution are carried by storm water runoff, or the water that runs over the ground during a rainstorm,and directly into the River. Storm water picks up pollutants in the form of fertilizers pesticides oil and various chemicals and bacteria from animal waste . The storm water flows through storm drains into the Clinton River without treatment. Therefore , the health of the river is affected by activities in the entire watershed.

## Slide 17: River Water Quality
Historical Water Quality Problems:
  Contaminated sediments
  Industrial & municipal discharges
  Flooding
Current Water Quality Problems:
  Bacterial contamination from sewer overflows and failing septic systems
  Contaminated sediments persist
  But what is the single greatest source of impairments in the our local major rivers?
STORMWATER
POLLUTION

## Slide 18
Why is stormwater a problem?
Runoff enters storm drain…
Storm drain discharges to waterway…
Pollutants fall on paved surfaces & lawns…
Dirt, oils, metals, salts
Dirt from construction sites
…resulting in water quality problems…
Animal waste, fertilizers, pesticides
…and impairment of aesthetic & recreational values

## Slide 19
The many faces of
stormwater pollution…
Grease, oils &
metals
Erosion & sedimentation
Bacteria & nutrients

## Slide 20: Impervious Surfaces and runoff
Notes: 20
In an urban environment where does runoff go can he concrete absorb it? What if there are no bodies of water around do parking lots and roads just flood? See if you can get the students to come up with storm drains if not go to next slide

## Slide 21
Imperviousness Increases Stormwater Runoff
1) The rooftops under which we live, work, and shop, and the transport system (roads, driveways, and parking lots) that we use to get from one roof to another are impervious surfaces (water can’t absorb through them).

## Slide 22
Stormwater can turn a
healthy river…
…into an unhealthy one.

## Slide 23
They connect to the
Great Lakes…

## Slide 24
…And to the rest of the World

## Slide 25: So what can we do to limit this impact?

## Slide 26
Don’t dump anything down storm drains
Don’t use pesticides/fertilizers, or sparingly use
Use car wash or wash on grass.
Pick up animal waste.
Don’t litter
Native plants
Rain barrel
Sweep, don’t hose
Dispose of hazardous chemicals properly
Label storm drains
Notes: The important thing to remember….is that whatever goes into our storm drains flows into our lakes and streams. See this picture. This is a woman hosing her trash into the storm drain. The storm drain is on the water. In real life, it may not look like this, but it’s the same thing.

## Slide 27
Stream Leaders Program Overview

## Slide 28
  1. To understand and keep watch of the impacts humans can have in their watersheds.
  2. Once data is collected, people can use the data to monitor future changes and to help correct negative impacts we may have imposed.
  3. Michigan streams are part of the Great Lakes Basin (big watershed).
  4. To educate you (students) about the importance of this precious resource.
So Why Should We Monitor Streams?
Notes: First explain some reasons for why people monitor water quality.

## Slide 29: What do We Monitor?
  1. Physical Assessment
  2. Biological Indicators
  3. Water Chemistry
Notes: Explain we measure 3 different aspects or parameters of a stream. Physical and Biological: briefly explain these parameters, but let them know we will talk about it more the next time we are in. Water Chemistry: This is our focus today.

## Slide 30
Physical Habitat Monitoring Overview
Notes: Explain we measure 3 different aspects or parameters of a stream. Physical and Biological: briefly explain these parameters, but let them know we will talk about it more the next time we are in. Water Chemistry: This is our focus today.

## Slide 31
Stream Width
Estimate the width of the wet bank.
Notes: Explain we measure 3 different aspects or parameters of a stream. Physical and Biological: briefly explain these parameters, but let them know we will talk about it more the next time we are in. Water Chemistry: This is our focus today.

## Slide 32
Channelized?
Notes: Explain we measure 3 different aspects or parameters of a stream. Physical and Biological: briefly explain these parameters, but let them know we will talk about it more the next time we are in. Water Chemistry: This is our focus today.

## Slide 33
Water Color
Brown
Green
Grey
Notes: Explain we measure 3 different aspects or parameters of a stream. Physical and Biological: briefly explain these parameters, but let them know we will talk about it more the next time we are in. Water Chemistry: This is our focus today.

## Slide 34
Substrate Composition
SUBSTRATE (add to 100%)
% Boulder (<10”) % Cobble (2”-10”) % Gravel (1/4”-2”) % Sand (1/16”-1/4”) Artificial - manmade

## Slide 35
Substrate Examples

## Slide 36
Embeddedness
    The amount of sediment deposited on a rocky substrate
*

## Slide 37
Riparian Vegetation
    The area of vegetation between land and a river or stream.
*

## Slide 38
Stream Shading
Undercut banks
Overhanging branches

## Slide 39
Bank Erosion
Low
Moderate
Severe
    Water wearing away at the banks of a stream or river
*

## Slide 40
Stream Habitat
Riffle
Run

## Slide 41
Aquatic Plants
    At healthy levels, it provides cover for small animals such as aquatic insects, snails, and scuds, which are valuable fish food...
*
Filamentous Algae
    Excessive growth depletes the dissolved oxygen in the water and is a major contributor to fish deaths.
*

## Slide 42
Aquatic Plants
Duckweed
    Vascular plant! Not to be considered floating algae.
*
    The genus Wolffia has the smallest flower in the world!
*
    when nitrogen and phosphorous levels are high, these plants can completely take over the surface of the water, blocking out light, and lowering the oxygen levels in the water.
*
Floating Algae

## Slide 43
Land Use
North Branch Clinton River
ADJACENT LAND USES
Wetlands
Shrub or Old Field
Forest
Pasture
Crop Land
Animal Feeding Operation
Maintained Lawn
Impervious Surfaces
Disturbed Ground
No Vegetation
Main Branch Clinton River

## Slide 44
Examples of Adjacent Land Use

## Slide 45
Aquatic Macroinvertebrates

## Slide 46
What are Benthic Macroinvertebrates?
Benthic = bottom level (of a body of water)
Macro = large enough to be seen with the unaided eye
Invertebrate = without a backbone
Commonly referred to as: macros, benthos or bugs

## Slide 47
Why are Macroinvertebrates good indicators of stream health?
live in the water for all or most of their life
stay in areas suitable for their survival
are easy to collect
are easy to identify in a laboratory
often live for more than one year
have limited mobility
differ in their tolerance to amount of pollution
are indicators of environmental condition
!
!

## Slide 48
Macroinvertebrates
Often go unnoticed because of their size and habitat
Extremely important to a river ecosystem
  Primary food source for fish

## Slide 49
Macroinvertebrates: Group 1
Stonefly
Caddisfly
Water Penny
Riffle Beetle
Mayfly
Dobsonfly
Gilled Snail
  Pollution sensitive organisms found in good quality water
*

## Slide 50
Macroinvertebrates: Group 2
Crayfish
Sowbug
Dragonfly
Damselfly
Fishfly
Alderfly
Cranefly
Beetle
Net-spinning Caddisfly
  Somewhat pollution tolerant organisms found in good or fair quality water
*

## Slide 51
Macroinvertebrates: Group 3
Aquatic Worm
Midge fly
Black fly
Leech
Pouch/Pond snail
Other snails
  Pollution tolerant organisms found in any quality of water
*

## Slide 52
Equipment

## Slide 53
All Found in our Rivers, Streams and Lakes!

## Slide 54: Chemical Analysis
We will be measuring 8 different aspects of the water:
Dissolved Oxygen
Biochemical Oxygen Demand (BOD)
Coliform Bacteria
Nitrate
pH
Phosphate
Temperature
Turbidity
Sounds Fun Right?!
Notes: Just give them the list of the different parameters. You can explain them more in depth in the next couple slides.

## Slide 55
Dissolved Oxygen (DO): Required for respiration by various types of aquatic life. Optimal levels are 5 – 7ppm
    Percent Saturation: Colder water holds more Oxygen.
*
Biochemical Oxygen Demand (BOD): the quantity of dissolved oxygen used by bacteria.
Coliform Bacteria: Occurs naturally at low to no levels. Sources are from fecal contamination.
Nitrates: Nutrient for plant growth. Optimal levels are
< 4ppm
Notes: Demonstrate as many tests as you want (time permits). I would recommend to have a student assist just because the subject of water quality chemistry is not the most interesting to 9th graders.

## Slide 56
pH: Optimal levels are 6.5-8.2
Total Phosphate: Nutrient for plant growth. Optimal level is
< 0.03ppm
Turbidity: Measurement of the relative clarity of the water
Water Temperature: < 20oC is the optimal temp for sensitive macroinvertebrates, trout, and other cold water species
Notes: Explain the importance and significance of each of these parameters. Might want to tell them what ppm stands for (parts per million).

## Slide 57: Data Sheets:
Chemical 
Notes: Just go over the chemical data sheet briefly. Emphasize that it is not a worksheet, but just a way to track your results from your tests.
Next time we are here we will be going over the physical assessment and the biological monitoring.

## Slide 58
Questions?